## Slide 1: Revision
Long Tan Le
HCMC University of Technology
tanlong.ce@gmail.com

## Slide 2: Outline
Arithmetic Circuits
  Binary {Addition, Subtraction, Multiplication, Division}
  Number Representation
  Adders, Subtractors, BCD Adder, Carry Look-Ahead Adder
Counters & Registers
  Shift Register, Integrated-Circuit Registers
  Asynchronous Counter, Synchronous Counter
  Ring Counter, Johnson Counter
  ICs for Counters
MSI Logic Circuits
  Multiplexer , Demultiplexer
  Decoder, Encoder
  Comparator
  Logic Implementation using MSI circuits
  ICs for MSI Circuits
Chapter 1,2,3,4
Self-revision!

## Slide 3: Arithmetic Circuits
Topic 1

## Slide 4: Representation for Binary Number
Signed Magnitude
0 – Positive
1 – Negative
Only (n-1) bit used for storing value
the left most bit is considered as SIGN BIT

## Slide 5: Representation for Binary Number
1’s Complement
  Invert all bits (i.e. Change 1 as 0 and 0 as 1)
2’s Complement
  Invert all bits (i.e. Change 1 as 0 and 0 as 1)
  Add 1 to the result to the Least Significant Bit (LSB)

## Slide 6: Representation for Binary Number
1’s complement
Simple implementation which uses only NOT gates for each input bit.
Can be used for signed binary number representation but not suitable as ambiguous representation for number 0.
0 has two different representation one is -0 (e.g., 1 1111 in five bit register) and second is +0 (e.g., 0 0000 in five bit register).
For k bits register, positive largest number that can be stored is (2(k-1)-1) and negative lowest number that can be stored is -(2(k-1)-1).
end-around-carry-bit addition occurs in 1’s complement arithmetic operations. It added to the LSB of result.
1’s complement arithmetic operations are not easier than 2’s complement because of addition of end-around-carry-bit.
Sign extension is used for converting a signed integer from one size to another.
2’s complement
Uses NOT gate along with full adder for each input bit.
Can be used for signed binary number representation and most suitable as unambiguous representation for all numbers.
0 has only one representation for -0 and +0 (e.g., 0 0000 in five bit register). Zero (0) is considered as always positive (sign bit is 0)
For k bits register, positive largest number that can be stored is (2(k-1)-1) and negative lowest number that can be stored is -(2(k-1)).
end-around-carry-bit addition does not occur in 2’s complement arithmetic operations. It is ignored.
2’s complement arithmetic operations are much easier than 1’s complement because of there is no addition of end-around-carry-bit.
Sign extension is used for converting a signed integer from one size to another.

## Slide 8: Representation for Binary Number
1-2. Using 5 bits to represent each number, the representations of 13 and -13 in signed 2's complement integers: | 
A. 01101 & 11101 | C. 01101 & 10011
B. 01101 & 10010 | D. None of above
1-1. The 1’s complement form of the number 010011002? | 
A. 10110100 | C. 10110011
B. 00110010 | D. None of above
1-3. Sign extension from 5 bits to 8 bits represent -13 in signed 2's complement integers of the above question: | 
A. 00011101 | C. 00010011
B. 11110010 | D. None of above
Notes: 1-1. C
1-2. C
1-3. D - Sign Extension: The operation of increasing the number of bits of a binary number while preserving the number's sign (positive (0)/negative (1)) and value.

## Slide 9: Adding Two 1-bit Numbers
Performs the addition of two binary bits.
Four possible operations:
  0+0=0
  0+1=1
  1+0=1
  1+1=10
Circuit implementation requires 2 outputs; one to indicate the sum and another to indicate the carry.

## Slide 10: Addition of Two n-bit numbers
We start from the lsb
Add the corresponding pair of bits and the carry in
Produce a sum bit and a carry out
1 0 1 1
0 1 0 1
1 0 0 0 0
1
1
1
1

## Slide 11: Subtraction (2’s Complement)
If we represent signed numbers in 2’s complement form, subtraction is the same as addition to negative (2’s complemented) number.

## Slide 12: Addition in the 2’s Complement System
Perform normal binary addition of magnitudes.
Notes: 2 positives
positive and negative under
positive and negative numbers greater than
2 negatives
Equal

## Slide 13: Full Adder from Half Adders
1-4. How many AND, OR and EX-OR gates are requires for the configuration of full adder? |  |  | 
A. 1, 2, 2 | B. 2, 1, 2 | C. 3, 1, 2 | D. 4, 0 ,1
Notes: 1-4. B

## Slide 14: Adders & Subtractors
1-5. Half-adders have a major limitation in that they cannot:
A. Accept a carry from a present stage
B. Accept a carry bit from a next stage
C. Accept a carry bit from a previous stage
D. Accept a carry bit from the following stages
1-6. Full subtractor is used to perform subtraction of? |  |  | 
A. 2 bits | B. 3 bits | C. 4 bits | D. 8 bits
1-7. The output of a full subtractor is same as: |  | 
A. Half Adder | B. Full Adder | C. Half Subtractor
Notes: 1-5. C
1-6. B
1-7. B

## Slide 15: Multiplication & Division

## Slide 16: Multiplication & Division

## Slide 17: Multiplication & Division
1-8. Perform multiplication of the binary number: 01001 x 01011 | 
A. 001100011 | C. 010100110
B. 110011100 | D. 101010111
1-9. The quotient of 111101 ÷ 1001 is | 
A. 0010 | C. 1100
B. 1010 | D. 0011
1-10. In binary division process, a series of performed operations is said to be of | 
A. Additions | C. Multiplications
B. Subtractions | D. Complement
Notes: A
D
B

## Slide 18: BCD Adder
BCD Adder
When the sum of two digits is less than or equal to 9 then the ordinary 4-bit adder can be used
But if the sum of two digits is greater than 9 then a correction must be added “i.e. adding 0110”
We need to design a circuit that is capable of doing the correct addition

## Slide 19: BCD Adder

## Slide 20: Carry Look Ahead (CLA) Adder
Used in most ALU designs
Faster than ripple carry logic adders or full adders
  Especially when adding a large number of bits.
Be able to generate carries before the sum
  Using the Carry Propagation (Pi) and Carry Generation (Gi) logic to make addition much faster.
Notes:   Carry Generation occurs when both inputs are 1
  Carry Propagation occurs when input is rippled to the output carry
  Where Gi is a carry generate which produces the carry when both Ai, Bi are one regardless of the input carry. Pi is a carry propagate and it is associate with the propagation of carry from Ci to Ci +1.

## Slide 21: Carry Look Ahead (CLA) Adder
Notes:   Carry Generation occurs when both inputs are 1
  Carry Propagation occurs when input is rippled to the output carry

## Slide 22: Other Adders
1-11. One of the advantages of the fast carry or look-ahead carry circuits found in most 4-bit parallel-adder circuits
A. Add a 1 to complemented inputs
B. Increase ripple delay
C. Determine sign and magnitude
D. Reduce propagation delay
1-12. The carry generate (CG) and carry propagate (CP) function of the Carry Look-Ahead adder is
A. CG = A or B, CP = A xor B
B. CG = A xor B, CP = A or B
C. CG = A and B, CP = A xor B
D. CG = A and B, CP = A or B
Notes: D
C

## Slide 23: Counters and Registers
Topic 2

## Slide 24: Registers
2-1. A register is defined as
A. The group of latches for storing one bit of information
B. The group of latches for storing n-bit of information
C. The group of flip-flops suitable for storing one bit of information
D. The group of flip-flops suitable for storing binary information
2-2. A shift register is defined as
A. The register capable of shifting information to another register
B. The register capable of shifting information either to the right or to the left
C. The register capable of shifting information to the right only
D. The register capable of shifting information to the left only
Notes: D: Each flip-flop is a binary cell capable of storing one bit of information
B: A register in which data can be shifted only in one direction is called unidirectional shift register, while if data can shifted in both directions, it is known as a bidirectional shift register.

## Slide 25: Registers
2-3. The full form of SIPO is | 
A. Serial-in Parallel-out | C. Serial-in Serial-out
B. Parallel-in Serial-out | D. Serial-in Peripheral-out
2-4. The group of bits 11001 is serially shifted (right-most bit first) into a 5-bit parallel output shift register with an initial state 01110. After three clock pulses, the register contains? | 
A. 01110 | C. 00101
B. 00001 | D. 00110
2-5. With a 200 KHz clock frequency, eight bits can be serially entered into a shift register in ? | 
A. 4 μs | C. 400 μs
B. 40 μs | D. 40 ms
Notes: A: There are 4 types of shift registers, viz., Serial-In/Serial-Out, Serial-In/Parallel-Out, Parallel-In/Serial-Out and Parallel-In/Parallel-Out.
C: 01110 -> 10111 -> 01011 -> 00101
B: Explanation: f = 200 KHZ; T = (1/200) m sec = (1/0.2) micro-sec = 5 micro-sec; In serial transmission, data enters one bit at a time. After 8 clock cycles only 8 bit will be loaded = 8 * 5 = 40 micro-sec.

## Slide 26: Asynchronous (Ripple) Counter
This type of counter is easiest to design, and requires the least amount of hardware
Called Asynchronous
Called Ripple
The flip-flops are not driven by the same clock signal
Propagation Delay causes Ripple Effect
Can lead to unwanted transitions
Glitches are possible

## Slide 27: Design a Ripple Counter
J & K at HIGH level
Use negative edge triggered (NGT) FFs:
Connect Q output of the previous to CLK input of the next
Use positive edge triggered (PGT) FFs:
Connect Q’ output of the previous to CLK input of the next
Up Counter
using
JK FF

## Slide 28: Design a Ripple Counter
Suppose we want to design a module-M counter
  Counter will count up from 0 to M-1, and then back 0
Basic idea:
We first design a full-modulus ripple counter with (ceiling) flip-flops (e.g.: 4 FF -> MOD-16)
We first design a full-modulus ripple counter with ⌈log_2⁡𝑀 ⌉ (ceiling) flip-flops (e.g.: 4 FF -> MOD-16)
Then we design a gating circuit, which takes inputs from the counter outputs, and generate a 0 whenever the count value reaches M
Connect the output of the gating circuit to the CLR’ inputs of the flip-flops
Then we design a gating circuit, which takes inputs from the counter outputs, and generate a 0 whenever the count value reaches M
Connect the output of the gating circuit to the CLR’ inputs of the flip-flops

## Slide 29: Design a Ripple Counter
Example: Design a MOD – 10 (Decade) Up Ripple Counter using JK Flip-Flop
Reset state

## Slide 30: Design a Ripple Counter
Glitches: Temporary False / Unwanted outputs

## Slide 31: Duty Cycle
The percentage of time a digital signal is ON over an interval or period of time

## Slide 32: Ripple Counters
2-6. Ripple counter’s speed is limited by the propagation delay of | 
A. Each flip-flop | C. The flip-flops only with gates
B. All flip-flops and gates | D. Only circuit gates
2-7. The duty cycle of the most significant bit from a 4-bit (0–9) BCD counter is |  |  | 
A. 20% | B. 50% | C. 10% | D. 50%
2-8. A 5-bit asynchronous binary counter is made up of five flip-flops, each with a 12 ns propagation delay | 
A. 12 ms | C. 48 ns
B. 24 ns | D. 60 ns
Notes: A - A ripple counter is something that is derived by other flip-flops. It’s like a series of Flip Flops. The output of one FF becomes the input of the next. Because ripple counter is composed of FF only and no gates are there other than FF, so only propagation delay of FF will be taken into account. Propagation delay refers to the amount of time taken in producing an output when the input is altered
A- There are 10 states, out of which MSB is high only for (1000, 1001) 2 times. Hence duty cycle is 2/10*100 = 20%. Since the duty cycle is the ratio of on-time to the total time.
D- Since a counter is constructed using flip-flops, therefore, the propagation delay in the counter occurs only due to the flip-flops. Each bit has propagation delay = 12ns. So, 5 bits = 12ns * 5 = 60ns.

## Slide 33: Ripple Counter
2-9. Chose a TRUE statement
The up counter with MOD-12
The down counter with MOD-9
The down counter with MOD-13
The up counter with MOD-11
Notes: D - Reset state: DCBA = 1011 (11)

## Slide 34: Ripple Counter
2-10. Determine the frequency of output C
CLK/8 C. CLK/12
CLK/11 D. CLK/13
2-11. Determine Duty Cycle (HIGH) of output C.
A. 50% C. 36.36%
B. 33.33% D. 18.18%
Notes: B: 1111000000
C: 4(1)/11

## Slide 35: Ripple Counter
2-12. Determine the output that has glitches.
Output A
Output B
Output C
Output D
Notes: A: DCBA (1001 -> 1010 -> (1011) 0000

## Slide 36: Cascading Ripple Counter
2-13. List which pins need to be connected together on two 74293 to make a MOD-60 counter
Notes: IC 74293: MOD 2 x MOD 8 (MOD-16) Ripple Counter

## Slide 37: Cascading Ripple Counter
2-13. List which pins need to be connected together on two 74293 to make a MOD-60 counter

## Slide 38: Cascading Ripple Counter
2-14. Design an asynchronous counter MOD-40 (4x10) using only 74LS293 ICs. (Do it yourself!)

## Slide 39: Cascading Ripple Counter
2-15. Given the following counter circuit
(Do it yourself!)
With the frequency of the clock signal fCLK = 35 KHz
(a) What is the MOD of the counter ?
(b) Determine the frequency of Q3 of U1?
(c) Determine the frequency of Q2 of U2?
(d) In the Q3, Q2, Q1, Q0 signals of U1 and U2, which signals are glitches?
(e) Determine duty cycle of Q2 of U2?

## Slide 40: Synchronous Counter
All flip-flops are simultaneously clocked by an external clock.
Synchronous counters are faster than asynchronous counters because of the simultaneous clocking.
Synchronous counters are an example of a state machines design.

## Slide 41: Design a Synchronous Counter
1. Determine the # of FFs needed to support the counting sequence’s highest #.
2. Build a State Transition Diagram. Be sure to include all states.
3. Build a State/Excitation Truth Table.
4. Simplify expressions for J and K inputs for each F/F on K-Maps.
5. Implement the Synchronous Counter/State Machine Circuit. .

## Slide 42: Design a Synchronous Counter
Flip-Flop Transition Tables

## Slide 43: Design a Synchronous Counter
For the following stage diagram, design a synchronous counter using D Flip-Flops
(A: LSB, D: MSB)
0000
0001
0110
0111
1000
1001
1110
1111
Other states
Notes: B
D

## Slide 44: Design a Synchronous Counter
For the following stage diagram, design a synchronous counter using D Flip-Flops (A: LSB, D: MSB)
Present State |  |  |  | Next State |  |  |  | Output |  |  | 
D | C | B | A | D | C | B | A | DD | DC | DB | DA
State table

## Slide 45
Present State |  |  |  | Next State |  |  |  | Control Signal |  |  | 
D | C | B | A | D | C | B | A | DD | DC | DB | DA
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: B
D

## Slide 46: Design a Synchronous Counter
For the following stage diagram, design a synchronous counter using D Flip-Flops (A: LSB, D: MSB)
DD=
Dc=
DB=
DA=
K-maps

## Slide 47: Design a Synchronous Counter
For the following stage diagram, design a synchronous counter using D Flip-Flops (A: LSB, D: MSB)
Implement the logic circuit using D Flip-Flops

## Slide 48: Design a Synchronous Counter
2-16. Design a ripple counter, MOD-12, up counter, using J-K Flip-Flop and D Flip-Flop
2-17. Use J-K Flip-Flop and D Flip-Flop to design an asynchronous down counter as follows
6 → 5 → 4 → 3 → 2 → 1 → 6 → ...
2-18. Use J-K Flip-Flop to design a synchronous counter circuits according to the following transition diagram

## Slide 49: Ring & Johnson Counter
Ring Counter

## Slide 50: Ring & Johnson Counter
Johnson Counter

## Slide 51: Ring & Johnson Counter
2-19. On the fifth clock pulse, a 4-bit Johnson sequence is Q0 = 0, Q1 = 1, Q2 = 1, and Q3 = 1. On the sixth clock pulse, the sequence is….
Q0 = 1, Q1 = 0, Q2 = 0, and Q3 = 0
Q0 = 1, Q1 = 1, Q2 = 1, and Q3 = 0
Q0 = 0, Q1 = 0, Q2 = 1, and Q3 = 1
Q0 = 0, Q1 = 0, Q2 = 0, and Q3 = 1
Notes: C

## Slide 52: Ring & Johnson Counter
2-20. What is the difference between a ring shift counter and a Johnson shift counter? | 
A. There is no difference | C. The feedback is reversed
B. A ring is faster | D. The Johnson is faster
2-21. In a 6-bit Johnson counter sequence there are a total of how many states, or bit patterns ? | 
A. 2 | C. 12
B. 6 | D. 24
2-22. A modulus – 12 ring counter requires a minimum of | 
A. 10 Flip-flops | C. 6 Flip-flops
B. 12 Flip-flops | D. 2 Flip-flops
Notes: C
C
B

## Slide 53: Others
2-23. A MOD-16 ripple counter is holding the count 10012. What will the count be after 31 clock pulses? | 
A. 10002 | C. 10112
B. 10102 | D. 11012
2-24. A MOD-12 and a MOD-10 counter are cascaded. Determine the output frequency if the input clock frequency is 60 MHz | 
A. 500 kHz | C. 6 MHz
B. 1500 kHz | D. 5 MHz
2-25. A BCD counter is a | 
A. Binary Counter | C. Decade Counter
B. Full-modulus Counter | D. Divide-by-10 Counter
Notes: A
A
C

## Slide 54: Others
2-26. Give the circuit and waveform respectively. Is the waveform Correct or Not Correct? Explain why?
Notes: C

## Slide 55: MSI Logic circuits
Topic 3

## Slide 56: MSI Devices
Medium Scale Integration (MSI)
  Using a few tens to hundreds of logic gates.
Used as discrete devices packed in a single Integrated Circuit (IC),
Building blocks for more complex devices such as memory devices or microprocessors.
Some typical MSI devices are the following:
  Encoders and Decoders
  Multiplexers and Demultiplexers
  Comparator
Notes: - Adders, Registers, Counters are also types of MSI

## Slide 57: Examples of MSI Devices
Decimal to BCD Encoder
BCD to Decimal Decoder
4-to-1 Multiplexer

## Slide 58: Multiplexer (MUX)
A MUX has a
  2N data inputs,
  N control inputs
  One output
The select lines determine which input is connected to the output.
MUX Types
   2-to-1 (1 select line)
   4-to-1 (2 select lines)
   8-to-1 (3 select lines)
   16-to-1 (4 select lines)
Multiplexer
Block Diagram
Select
Lines
Inputs
(sources)
Output
(destination)
1
2N
N
MUX

## Slide 59: Typical Application of a MUX
MP3 Player
Docking Station
Laptop
Sound Card
Digital
Satellite
Digital
Cable TV
Surround Sound System
MUX
D0
D1
D2
D3
Y
B | A | Selected Source
0 | 0 | MP3
0 | 1 | Laptop
1 | 0 | Satellite
1 | 1 | Cable TV
Multiple Sources
Single Destination
Selector

## Slide 60: Multiplexer

## Slide 61: Multiplexer

## Slide 62: Multiplexer

## Slide 63: Logic Implementation using MUX
A 2n-to-1 MUX
  Can be used to implement ANY function of n variables
  Can be used to implement SOME functions of (n + 1) variables

## Slide 64: Logic Implementation using MUX
Example:
= A’B’C’ + A’B’C + ABC’ + ABC
= A’B’(C’) + A’B’(C) + AB(0) + AB(1)

## Slide 65: Logic Implementation using MUX
3-1. Implementing the following function as a 4-to-1 MUX
Notes: - S1(B), S0(C),

## Slide 66: Logic Implementation using MUX
3-1. Implementing the following function as a 4-to-1 MUX
B
C
F
F =
 | I0(B’C’) | I1(B’C) | I2(BC’) | I3(BC)
A’ | 1 | 1 | 1 | 0
A | 0 | 1 | 1 | 1
 | A’ | 1 | 1 | A
1
1
A’
A

## Slide 67: MSI
3-2. Implement following function using MUX:

## Slide 68: MSI
3-2. Implement following function using MUX:

## Slide 69: Demultiplexer (DEMUX)
A digital switch with
  One input (source)
  N control inputs
  2N outputs (destinations).
The select lines determine which output the input is connected to.
DEMUX Types
   1-to-2 (1 select line)
   1-to-4 (2 select lines)
   1-to-8 (3 select lines)
   1-to-16 (4 select lines)
Demultiplexer
Block Diagram
Select
Lines
Input
(source)
Outputs
(destinations)
2N
1
N
DEMUX
Notes: This slide explains the function of a demultiplexer.

## Slide 70: Typical Application of a DEMUX
Single Source
Multiple Destinations
Selector
D0
D1
D2
D3
X
DEMUX
B | A | Selected Destination
0 | 0 | B/W Laser Printer
0 | 1 | Fax Machine
1 | 0 | Color Inkjet Printer
1 | 1 | Pen Plotter
B/W Laser
Printer
Color Inkjet
Printer
Pen
Plotter
Fax
Machine
Notes: This slide shows a typical application of a demultiplexer (in this case a 1-to-4 DEMUX). Ask students to share other common applications of DEMUXs.

## Slide 71: Logic Implementation using Demux

## Slide 72: Decoders
A decoder has
  N inputs
  2N outputs
Only one of the outputs is enabled at a time.
  The output enabled is the one specified by the binary number formed at the inputs of the decoder.
Notes: On the circuit below, the inputs of the decoder are connected on three switches, forming the number 5 [(101)2], thus only the lamp #5 will be ON

## Slide 73: 2 to 4 Line Decoder

## Slide 74: 3 to 8 Line Decoder

## Slide 75: Decoders
3-3. Which statement below best describes the function of a decoder?
A decoder will convert a decimal number into the proper binary equivalent.
A decoder will convert a binary number into a specific output representing a particular character or digit.
Decoders are used to prevent improper operation of digital systems.
Decoders are special ICs that are used to make it possible for one brand of computer to talk to another.
Notes: B

## Slide 76: Decoders
3-4. Output 5 of a 74138 octal decoder is selected when it is enabled by a data input of:
A0 = 1, A1 = 1, A2 = 0
A0 = 1, A1 = 0, A2 = 1
A0 = 0, A1 = 1, A2 = 0
A0 = 1, A1 = 0, A2 = 0
Notes: B

## Slide 77: Logic Implementation using Decoder
3-5. Implement following function with decoder:

## Slide 78: Logic Implementation using Decoder
3-7. Using a 3-to-8 line decoder, design a logic circuit to realize the following Boolean function
3-6. Using a 2-to-4 line decoder, design a logic circuit to realize the following Boolean function

## Slide 79: Encoders
An encoder has
  2N inputs
  N outputs
Performs the inverse operation of a decoder

## Slide 80: Magnitude Comparator
Compares two input binary quantities and generates outputs to indicate which one has the greater magnitude

## Slide 81: Magnitude Comparator
3-8. What are the outputs of a 7485 four-bit magnitude comparator when the inputs are A = 1001 and B = 1010?
A < B is 1; A = B is 0; A > B is 1
A < B is 0; A = B is 1; A > B is 0
A < B is 0; A = B is 0; A > B is 1
A < B is 1; A = B is 0; A > B is 0
3-9. Which is the decimal number for the BCD number, 10110110 ?
182
36
116
10110110 is not a valid BCD number
Notes: D
D

## Slide 82: Others
3-10. Determine the correct output for the multiplexer and its associated timing diagram given below.
Ya
Yb
Yc
Yd
Notes: D